## Slide 1
ITEM | Spec | Remarks
Processor | 128 Core NIVIDA Maxwell GPU Quad core ARM A57 CPU 4GB 64bit LPDDR4 | 
Network | 10/100/1000Base-T Ethernet | 
Power | DC5V, 4A | 
I/O | USB 3.0 Type A, 4Ea USB2.0 micro–B, 4Ea HDMI/Display Port Gigabit Ethernet GPIO, I2C, SPI, UART | 
SD card | Micro SD | 
Video Encoder | 4K@30 ¦ 4x1080P@30 ¦ 9x720p@30(H.264/H.265) | 
Video Decoder | 4K@60 ¦ 2x4K@30¦ 8x1080P30 ¦ 18x720p@30(H.264/H.265) | 
AI Algorithm | Smoke & fire | 
IP Camera | RTSP | 
Class of Detection | Black smoke occurrence Gray smoke occurrence White smoke occurrence Fire(flame) occurrence Cloud Fog(smoke) Lighting Sunlight Wobbly white object Leaves, grass, etc, shaken by the wind Non(Irrelevant) | 
Recognition Speed | 76~85ms/frame(About 11~13FPS) | 
Fire frame detection | More than 0.3% of screen size(85x85pixels at 1920x1080 resolutions) | 
F1-Score | 0.861952 | 
Dimension mm(Board) | TBD | 
Fire and Smoke Detection at AI edgy box : ADK-JN-FIRE
Our AI model, which possesses 1.7 million fire and smoke image data, was trained on a selected 200,000 images. It classifies into 11 different categories, including false positives due to scenes like fireworks and smoke. It demonstrates a high performance with an average precision (mAP) of 0.90019. Operating on a Jetson Nano, it achieves recognition speeds of 76-85ms per frame, which is 1/20th the performance of a standard AI PC. It boasts a flame detection rate of over 0.3% of the screen size and can detect as low as 0.1% for clean flames.
Additionally, it offers cross-platform compatibility, supporting Windows, Linux, and ARM architectures.